## Slide 1
U.S. Department of Energy Building Energy Codes Program
2018 National Energy Codes Conference
Pre-Conference, July 15, 2018
Austin, TX
AIA Provider # 1014
AIA Course # PRECDS3
ICC Preferred Education Provider
COMcheck Basics
Bob Schultz

## Slide 2: AIA and ICC Continuing Education Provider
Continuing Education Credits Earned on Completion of this Live Session:
2.0 LU/HSWs will be reported to AIA CES for AIA members.
0.2 ICC CEUs for ICC members must self-report to ICC with the Certificate of Completion.
Certificates of Completion for self-reporting to your professional organization for non-AIA and non-ICC members are available upon request.
This course is registered with AIA CES and ICC PP for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA or ICC of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product.
________________________________________
AIA and ICC Continuing Education Provider

## Slide 3
Course
Description
Basics of using COMcheck software, reviewing generated compliance reports, and the latest and greatest new features.

## Slide 4
Learning
Objectives
Obtain an overview of the basic functions and how COMcheck calculates compliance for the building envelope, interior and exterior lighting, and mechanical.
Be able to identify the construction specifications needed to complete a compliance calculation in the software.
Learn how to enter the building envelope, lighting and mechanical components into the software.
Understand how the compliance reports are created and what they entail.
At the end of the this course, participants will be able to:

## Slide 5: COMcheck Basics
bob schultz
2018 Department of Energy National Energy Codes Conference
Building Energy Codes Program
July 15, 2018
Notes: PNNL develops and supports the CheckTools suite of software
Residential projects – REScheck
Commercial projects - COMcheck
Why do we do this?
Compliance: Provide technical assistance to states to implement building energy codes including increasing and verifying compliance to ensure consumer benefits (42 USC 6833), develop software to support a streamlined compliance process, provide objective information resources and technical guidance to states and localities to increase code compliance.

## Slide 6: CheckTools Current Use Scenario
BECP Tools used only during “Demonstrate Compliance” Stage
Demonstrate Compliance
Collect Data
Check Compliance
Plan Review
Review Software Input
Review Mandatory Requirements
Field Inspection
Verify compliance of inspection checklist items
Prepare Input
Generate Compliance Report
Check Compliance Results
Approve compliance
Builder Architect Designer
Plan Reviewer
Field Inspector
Paper/PDF
Paper/PDF

## Slide 7: COMcheck Compliance Methods
Mandatory
Provisions
(required for most compliance options)
Building System
Compliance Options
Energy Code Compliance
Prescriptive Option
Energy Cost Budget: Performance Simulation
Trade Off Option
Envelope
HVAC
Lighting
SWH
Power
Other

## Slide 8: Envelope Trade-Off Methods (cont.)
ASHRAE 90.1 (Pre-2013) Normative Appendix C Methodology for Building Envelope Trade-Off Option
  90.1-2007/2010
  2009/2012 IECC
ASHRAE 90.1-2013/2016 Appendix C has limited performance method (EnergyPlus)
2015/2018 IECC Component Performance Alternative (Total UA)

## Slide 9: Commercial Energy Code Envelope Trade-Off Methods
90.1-2013/2016 Appendix C Envelope Trade-Off Methodology
Envelope components are assigned to isolated thermal zones based on
  Building area types (BAT)
  Space conditioning categories (SCC)
  Orientation, type, and property etc.
  One packaged single-zone AC per zone
Non-envelope model inputs are held constant (lighting, HVAC, schedules etc.) between Proposed and Base models.
2015/2018 Component Performance Method Criteria
Envelope assemblies must pass on ‘hybrid’ Total UA based criteria
Area-weighted fenestration U-factor
SHGC prescriptive requirement

## Slide 10: Project Types
New Construction:
  Trade-off compliance method
  Prescriptive – Oregon only
Addition
  Trade-off compliance method
  Prescriptive – Oregon only
Alteration
  Prescriptive compliance
Notes: The Trade-off compliance approach is used for New Construction and Addition. The prescriptive compliance option is used for Alteration.

## Slide 11: Lighting Compliance Methods
Mandatory requirements: Controls, Switching
Interior/Exterior lighting power requirements
  Complies if total connected power <= lighting power allowance
Proposed Wattage
Allowed Wattage
≤
Allowed Wattage

## Slide 12: Mechanical/Service Hot Water Compliance
Efficiency requirements
Economizer requirements
Fan Power Limitation
Mandatory requirements
No compliance metric available
Allowed Wattage
Allowed Wattage

## Slide 13: COMcheck Project Specification Steps
Project
Building Envelope Components
Lighting
Mechanical
Requirements Reports

## Slide 14: Info You’ll Need
Energy Code
Builder and project location
Area take-offs for envelope assemblies
Insulation R-values, fenestration performance data
Lighting fixture details
Heating and cooling system details
Service water heating details

## Slide 15: www.energycodes.gov

## Slide 16
COMcheck
“Desktop”
Web

## Slide 17
Can exchange files between desktop and web
  Log in to web
  My Projects
Desktop/Web Data Exchange
Upload from desktop to web account
Download from web account to desktop

## Slide 18: COMcheck Basics: Color cues and feedback
Red
Green
Blue
Status bar
Compliance bar

## Slide 19: COMcheck Basics: Menus and Toolbars
General
File options
Version update check
Project
Code/location
Envelope
Applicant
Project details
Reports
Signatures
Upload usage data
Email reports

## Slide 20: COMcheck Basics: Options Menu
Options menu is tab dependent and code dependent
Exemptions/Allowances
Comments
Notes: The software allows you to enter building components with or without considering the component orientation (north, south, east, and west). Initially, the orientation option is turned off.
Projection Factor lets you account for the shading impact of horizontal overhangs or canopies that project outward from the plane of the window. The projection factor is the ratio of the distance the overhang projects from the window surface to its height above the sill of the window it shades. Only enter overhangs that are shown on the building plans.

## Slide 21: Project Screen

## Slide 22: Project: Code and Location
Appropriate Code
Location

## Slide 23: Project: Project Type
New Construction
Addition
Alteration
Notes: The Trade-off compliance approach is used for New Construction and Addition. The prescriptive compliance option is used for Alteration.

## Slide 24: Project: Alteration project type explained
Projects involve changes to or replacement of
  Existing building components that are part of building envelope
  Lighting, heating, ventilating, air conditioning, and water-heating equipment
Specify only those envelope components, lighting fixtures, or mechanical systems/equipment that will exist upon completion of the project.
Alteration detail dialogs
  Specify exemptions if applicable
  Additional qualifications may be required (e.g., Window/wall ratio)
Compliance shown as Pass/Fail for Envelope and Lighting

## Slide 25: Compliance Options (IECC only)
Efficiency Options
  High performance power (2012/2015/2018)
  Reduced lighting power (2012/2015/2018)
  On-site renewable energy (2012/2015/2018)
  High performance SWH (2015/2018)
  Enhanced interior lighting controls (2015/2018)
  Dedicated outdoor air system (2015/2018)
  Enhanced Envelope Performance (2018)
  Reduced Air Infiltration (2018)
Air Barrier Options (IECC 2012+, climate zone dependent)
  Air barrier permeability
  Assembly permeability
  Air leakage test

## Slide 26: Project: Project Details
Optional
Sections
  Title/Site/Permit
  Owner/Agent
  Designer/Contractor
Included on report

## Slide 27: Project: Building Envelope Area Types
Primarily impacts envelope compliance
Whole building types that describe the envelope (separating conditioned and unconditioned spaces)
Space conditioning type
  Nonresidential
  Residential
  Semiheated (no mechanical cooling) – 90.1 only
Notes: The new feature enables envelope assemblies to be assigned to a specific space conditioning type so specific requirements for that assembly can be applied and so internal loads of the building can be assigned by space conditioning.

## Slide 28: Project: Interior Lighting Method and Area Types
Method determines lighting power density and allowances
Area category allows for more detailed space representation
Notes: The new feature enables envelope assemblies to be assigned to a specific space conditioning type so specific requirements for that assembly can be applied and so internal loads of the building can be assigned by space conditioning.

## Slide 29: Interior Lighting: Methods
Selected method determines lighting power densities in interior lighting and exterior lighting screens
  based on code, method, and applications selected on the Project screen

## Slide 30: Project: Exterior Lighting Area Types
Zone and area type determine:
  Lighting power density
  Units
  Tradability
Notes: The new feature enables envelope assemblies to be assigned to a specific space conditioning type so specific requirements for that assembly can be applied and so internal loads of the building can be assigned by space conditioning.

## Slide 31: Exterior Lighting: Tradable Applications
Tradable areas allow ‘unused’ allowable power to be traded between other tradable area (e.g., driveways and entry ways)
Generally based on length or area of application then summed
Notes: Tradable – for example, wattage allowed for parking lot lighting can be “traded” and used for canopy lighting.

## Slide 32: Exterior Lighting: Non-Tradable Applications
  Non-tradable areas/applications are “use it or lose it” (e.g., building façade lighting, ATM stations)
Notes: Nontradable – these applications have more specific security or task illuminance needs such as ATM machines, drive-up windows, emergency services

## Slide 33: Project Summary and example

## Slide 34: Envelope: Introduction
Cavity Insulation R-value – insulation placed between structural members
Continuous Insulation R-value – ‘continuous’ insulation across the structure (e.g., rigid insulation)

## Slide 35: Envelope: Opaque Assemblies
After you’ve entered building components, look at compliance result
  Look for fields with red text
  If TBD, look for missing data

## Slide 36: Envelope: Fenestration
NFRC site-built certified product
Performance evaluated (per NFRC guidelines)
Energy code defaults

## Slide 37: Envelope: 2015 IECC Fenestration Requirements
Menu View->Glazing Requirements

## Slide 38: Envelope: Summary
Don’t have to use every assembly type
Can group “like” components
Gross area (except slab-on-grade)
Use “Other” assembly as needed

## Slide 39: Lighting Compliance
Exemptions
Mandatory Requirements (Interior and Exterior)
Controls
Switching
Interior Lighting Power Limits
Whole Building
Additional Allowances
+
Efficiency
Space-by-Space
Exemptions
Exterior Lighting Power Limits
+
Total Connected Power
Interior Lighting Power Allowance
<
OR
Tradable
Non-Tradable
Total Connected Power
Exterior Lighting Power Allowance
<

## Slide 40: Interior Lighting: Spaces and Fixtures
Select space then Add Fixture button or Fixture Library
Fixture library preserves frequently used fixtures for future use
Allowed/Proposed wattage balance maintained
Notes: Only applicable to the desktop version as of March 2013

## Slide 41: Lighting Fixture Categories
Linear fluorescent
Compact fluorescent
HID
Incandescent
Halogen
Track lighting
LED
Induction
Notes: Induction lighting is a fluorescent type bulb without the metal electrical contacts used to conduct electricity from the fixture to the light-emitting gas inside the bulb. Induction is the process of transmitting energy via an electro-magnetic field. The light emitting gas inside the bulbs is excited, or energized when located within a sufficiently strong EMF, or electro-magnetic field, which is induced by passing alternating current through a coil, or inductor. This means that electricity-conducting metal contacts are unnecessary on the bulb, and the bulb will experience longer life.
The lamps are capable of saving 40% over fluorescents, and some models boast a life expectancy of up to 100,000 hours.

## Slide 42: Lighting: Exemptions and Allowances
Options menu
Exemptions
  Power for exempt fixtures is omitted from the proposed wattage
Allowances
  Allowed wattage for building increased by allowable amount

## Slide 43: Lighting: Exemptions and Allowances (cont)

## Slide 44: Exterior Lighting
Inputs will be based on code selected
Mandatory requirements
Exemptions
Total Connected Power
≤
Ext. Ltg. Power Allowance

## Slide 45: Exterior Lighting: Example
Lighting applications entered similar to interior lighting
Pay attention to tradable versus non-tradable criteria.

## Slide 46: Mechanical Systems
Limited means to determine compliance
Enter characteristics of
  HVAC system
  Plant
  Water heating
Characteristics you select determine which requirements apply
Notes: Mechanical works differently because most of the mechanical requirements are mandatory.
The characteristics you enter enable the software to exclude large numbers of requirements that don’t apply to your systems.
HVAC system refers to secondary HVAC systems, including controls, fans, terminal boxes, radiators, coils, and package HVAC equipment, not primary HVAC system components such as boilers, chillers, cooling towers, and pumps. The characteristics you select determine which requirements apply. Some of the inputs are interdependent.
Plant refers to primary HVAC components, such as boilers, chillers, cooling towers, and pumps.
Water heating – the selection (or deselection) of the checkboxes in this section determines which water heating requirements apply to your building.

## Slide 47: Mechanical Systems
Example of a typical duct furnace and split system
Notes: Mechanical works differently because most of the mechanical requirements are mandatory.
The characteristics you enter enable the software to exclude large numbers of requirements that don’t apply to your systems.
HVAC system refers to secondary HVAC systems, including controls, fans, terminal boxes, radiators, coils, and package HVAC equipment, not primary HVAC system components such as boilers, chillers, cooling towers, and pumps. The characteristics you select determine which requirements apply. Some of the inputs are interdependent.
Plant refers to primary HVAC components, such as boilers, chillers, cooling towers, and pumps.
Water heating – the selection (or deselection) of the checkboxes in this section determines which water heating requirements apply to your building.

## Slide 48: Mechanical: Fan Systems
Determines Fan Power Limitations compliance for each fan system
Motor nameplate HP and brake HP
  Brake HP includes pressure drop credits as applicable
Notes: Applicable only to the desktop version as of March 2013

## Slide 49: Requirements Tab – Goals
Ensure user is aware of applicable mandatory requirements and addresses each in the software
Provide better documentation for code officials

## Slide 50: Requirements Tab – How it Works
For each requirement, the user
  Chooses a “compliance option”
    Requirement will be Met
    Exempt or Exceptions
    Requirement is Not Applicable or Requirement Does Not Apply
  Notes how compliance for applicable requirements are documented
This information is shown on the report in the “Comments/ Assumptions” column of the Inspection Checklist

## Slide 51: Reports
File View / Print Report
Choices, choose any or all
  Envelope Compliance Certificate
  Interior Lighting Compliance Certificate
  Exterior Lighting Compliance Certificate
  Mechanical Compliance Certificate
First pages are the Compliance Certificate
Follow-on pages are the Inspection Checklists by phase of inspection
  Plan Review
  Footing/Foundation
  Rough-in
  Final

## Slide 52: Report – Compliance Certificate

## Slide 53: Reports – Compliance Certificate (cont)
Verify energy code, location, and construction type specifications

## Slide 54: Reports – Compliance Certificate (cont)
Verify Compliance Statement is Signed
Verify area, insulation R-values, and U-factors consistent with plans

## Slide 55: Reports – Inspection Checklist

## Slide 56
www.energycodes.gov

## Slide 57
COMcheck Page

## Slide 58: U.S. DOE: BECP Resources
Compliance software
Technical support
Code notes
Publications
Resource guides
Training materials www.energycodes.gov

## Slide 59: THANK YOU!
Building Energy Codes Program
www.energycodes.gov
BECP help desk
http://www.energycodes.gov/resource-center/help-desk