## Slide 1
Residential Provisions of the 2021 IECC
PNNL-SA-170339

## Slide 2: Outline
Overview of IECC Structure
Summary of what changed between 2018 and 2021 IECC
Focus on key energy related changes in the 2021 IECC
  Envelope
  Lighting
  HVAC
  SHW
  Performance Path/Energy Rating Index (ERI)
  Appendix RB for Zero Energy Homes
Notes: 2 minutes
Painstaking detail

## Slide 3: The Family of I-Codes
International Building Code
International Mechanical Code
International Fuel Gas Code
International Property Maintenance Code
International Fire Code
International Zoning Code
International Plumbing Code
International Existing Building Code
International Private Sewage Disposal Code
International Performance Code
International Residential Code
International Energy Conservation Code
International Wildlife-Urban Interface Code
ICC Performance Code for Buildings and Facilities
International Green Construction Code
Notes: The IECC is one of the International Codes. This code establishes minimum regulations for energy efficient buildings using prescriptive and performance related provisions.
The IECC contains energy provisions for both residential and commercial buildings.
  Building Envelope - focuses on air sealing, minimum insulation levels, and efficient glazing.
  Mechanical Systems - addresses equipment efficiency, HVAC controls and heating and cooling distribution.
  Electrical Systems - focuses on interior and exterior lighting wattage limits and controls for efficient lighting usage.
  Service Water Heating Systems - addresses water heating efficiency and hot water distribution.
Health and life safety take precedence.

## Slide 4: Why Care about the IECC?
  Energy codes and standards set minimum efficiency requirements for new and renovated buildings, assuring reductions in energy use and emissions over the life of the building. Energy codes are a subset of building codes, which establish baseline requirements and govern building construction.
  Code buildings are more comfortable and cost-effective to operate, assuring energy, economic and environmental benefits.
Notes: Energy Codes set the minimum efficiency requirements for new and existing buildings guaranteeing reductions in energy consumption and emissions. Also improve comfort and durability.
Subset of Building Codes which govern the construction of the buildings
Energy codes ensure savings as a result of efficient building design
Cost benefit with building efficiency into a new building as it is more costly to achieve higher efficiency in existing buildings
The Purpose of Building Energy Codes
Energy codes and standards set minimum efficiency requirements for new and renovated buildings, assuring reductions in energy use and emissions over the life of the building. Energy codes are a subset of building codes, which establish baseline requirements and govern building construction. Code buildings are more comfortable and cost-effective to operate, assuring energy, economic and environmental benefits. The reduction in energy expenditures also correlates to a mitigated dependency on foreign oil, impacting national security. In light of these fundamental environmental issues, economic challenges, and uncertain energy costs, building energy codes are a key component of sound public policy.
The Benefits of Building Energy Codes
It is estimated that by 2035, 75% of the building stock in the U. S. will be new or renovated.6 As a building's operation and environmental impact is largely determined by upfront decisions, energy codes present a unique opportunity to assure savings through efficient building design, technologies, and construction practices. Once a building is constructed, it is significantly more expensive to achieve higher efficiency levels. Energy codes ensure that a building's energy use is including as a fundamental part of the design and construction process; making this early investment in energy efficiency will pay dividends to owners and occupants for years into the future.
Who benefits from energy codes?
Consumers and homebuyers can be assured that they have purchased or rented a home that meets minimum standards for energy efficiency, and as a result will see significantly lower utility bills.
The construction industry can have a documented advantage over existing homes, as well as a level playing field, with respect to minimum energy efficiency requirements.
Code officials can be confident that new and renovated buildings are designed and built to meet industry standards for quality and comfort, thus improving consumer protection.
Utilities can benefit from supporting energy codes through access to cost-benefit data to use in determining future investments and attribution of savings to efficiency programs. Additionally, codes can provide better energy forecasting and decreased peak demand.
State and local governments can reduce energy demand and greenhouse gas emissions, while ensuring that their constituents live and work in comfortable buildings with low utility bills.

## Slide 5: Relationship Between IRC & IECC
IECC addresses only energy
IRC addresses all topics (structural, plumbing, etc.)
    Allows builder to carry only one code book
    Chapter 11 covers energy efficiency
As of 2015, IECC consolidated with IRC energy chapter (actually a change to the IRC, not the IECC).
IECC addresses both residential and commercial; IRC addresses subset of residential, detached one- and two-family dwellings and townhouses 3 stories or fewer
VS
Notes: IRC Chapter 11 is not a direct copy of the IECC residential provisions – there are some minor changes.

## Slide 6: Compliance Terminology
IECC Terminology
  Prescriptive
    Component-specific requirements that can be lessened or eliminated in trade for compensating improvements elsewhere
  Total Building Performance/Energy Rating Index
    Compares annual energy performance compared to a standard reference home.
  Note: Unlike simulated performance path, ERI path is not directly based on the prescriptive requirements
Some elements have “hard limits” AKA “trade-off limits” or "backstops"
  Puts limits on how far a component-specific prescriptive requirement can be reduced in trade-offs against other components

## Slide 7: Overview of Structure of the IECC
  Structure of the IECC

## Slide 8: Structure of the 2021 IECC
Ch. 1 Scope and Application / Administrative and Enforcement
Ch. 2 Definitions
Ch. 3 General Requirements
Ch. 4 Commercial Energy Efficiency
Ch. 5 Existing Buildings
Ch. 6 Referenced Standards
Appendices
Index
Commercial
Section
Residential
Section
Ch. 1 Scope and Application / Administrative and Enforcement
Ch. 2 Definitions
Ch. 3 General Requirements
Ch. 4 Residential Energy Efficiency
Ch. 5 Existing Buildings
Ch. 6 Referenced Standards
Appendices
Index

## Slide 9: Chapter 4 – Residential Energy Efficiency
Climate-Specific Requirements (mostly envelope)
  Roofs, walls, foundations R-values/U-factors
  U-factors of windows, doors, skylights
  Solar Heat Gain Coefficient
  Air leakage rate
  Duct leakage rate
Performance Based Alternatives
  Performance Compliance
  Energy Rating Index Compliance
Other Requirements (sometimes climate-specific)
  Infiltration control
  Duct insulation, sealing & testing, no use of building cavities
  HVAC controls
  Piping Insulation and circulating service hot water requirements
  Equipment sizing
  Dampers
  Lighting

## Slide 10: IECC Residential Compliance – 4 Pathway Options
ENERGY RATING INDEX (ERI)
U-factor (tradeoffs within individual components)
UA (tradeoffs between envelope components)
R-value (no tradeoffs)
Total Building Performance
R405
PRESCRIPTIVE
ERI
Compliance Alternative
R406
TOTAL BUILDING PERFORMANCE
TROPICAL CLIMATE REGION
R407
ADDITIONAL ENERGY EFFICIENCY R401.2.5
+ one option below
Notes: Compliance options:
Prescriptive
Total Building Performance
Energy Rating Index
Tropical Climate Region
The 2021 IECC removed use of the labels “prescriptive” and “mandatory” – now all requirements are identified within each path.
Additional Energy Efficiency requirements in R401.2.5 are applicable to all compliance paths.

## Slide 11: What Has Changed in the 2021 IECC?
Chart: 
  Here’s a summary

## Slide 12: Summary of Changes
Updated climate zone map to align with ASHRAE 169-2013
Additional efficiency options
Several increases in R-value (and corresponding decreases in U-factor)
  Wood frame wall insulation in CZ 4-5
  Slab insulation and depth in CZ 3-5
  Ceiling insulation in CZ 2-8
Reductions in U-factor
  Fenestration in CZ 2-4
  Fenestration U-factor of 0.32 for CZ 4C, 5-8 above 4000 ft elevation
Alternative options for
  Wood frame walls
  Basement walls
  Crawlspace walls
Notes: This is not an exhaustive list

## Slide 13: Summary of Changes, cont’d
New fenestration SHGC requirement in CZ 4C and 5
Maximum air leakage rate set to 5.0 ACH50 for tradeoffs
Lowered area-weighted maximum U-factor and SHGC
Removed duct testing exception for ducts in conditioned space
All permanently installed lighting fixtures to have high-efficacy lighting sources
Exterior lighting in low-rise multifamily buildings must comply with Section C405.4 Exterior Lighting Power Requirements
Exterior lighting controls
  Manual on/off switches with automatic shutoff
  Photosensor controls
  Timer switch
  Automatic shutoff allowing override to return to normal control within 24 hours

## Slide 14
  2021 IECC Detailed Slides

## Slide 15: Scope Section R101.4.1 - Mixed Residential and Commercial Buildings Section R101.5 - Compliance
Treat the residential building portion under the applicable residential code
Treat the commercial building portion under the commercial code
Code Official has final authority
  Compliance materials, software, worksheets
Notes: The residential and commercial building portions fall under two different scopes. Thus, two compliance submittals must be prepared using the appropriate calculations and forms from the respective codes for each. Residential = up to 3 stories.
Case by case basis.

## Slide 16: Scope Section R102.1 – Alternative Materials, Design, and Methods of Construction and Equipment
The code is not intended to prevent installation of any material or prohibit design or method of construction that is not specifically prescribed in this code
Such material, equipment, or design shall be approved by the code official
  Code official to state reasons in writing

## Slide 17: Scope/Construction Documents Section R103
Documentation shall be prepared by a registered design professional (where required)
Electronic media can be used
Information required:
  Insulation materials and R-values
  Fenestration U-factors, SHGC
  Area-weighted U-factor and SHGC calculations
  Mechanical, SWH, equipment types, sizes, and efficiencies
  Equipment and system controls
  Duct sealing, duct and pipe insulation and location
  Air sealing details
The building thermal envelope shall be represented
Notes: Documentation shall be prepared by a registered design professional (where required by statute by the code official)
No work shall be done on any part of the building beyond the point indicated in each successive inspection without first obtaining written approval of the code official.
No construction work shall be concealed without being inspected and approved.

## Slide 18: Scope Section R104-R109
Fees, R104
Inspections, R105
  Work remains visible and accessible for inspection
Notice of Approval, R106
Code Validity, R107
  Portions of code deemed to be illegal or void shall not affect the remainder of the code
Referenced codes and standards, R108
  Considered part of the requirements of the code, but IECC provisions take precedence
Stop Work Order, R109
  Authority of code official
  Failure to Comply subject to fine
Means of Appeals, R110
Notes: Life and safety take precedence. A couple of these will go into more detail in further slides, the next two slides touch a little bit more on two of these.

## Slide 19: Inspections Section R105
Construction work for which a permit is required is subject to inspection by code official or designated agent
Required inspections include:
  Footing and foundation
  Framing and rough-in
  Plumbing rough-in
  Mechanical rough-in
  Final

## Slide 20: Referenced Codes and Standards Section R108.1
Codes and standards listed in Chapter 5 are considered part of the requirements of this code to the “prescribed extent of each such reference and as further regulated in Sections R108.1.1 and R108.1.2”
Conflicts, R108.1.1 – where differences occur between this code and the referenced codes and standards, provisions of this code apply
Provisions in reference codes and standards, R108.1.2 – “where the extent of the reference to a referenced code or standard includes subject matter that is within the scope of this code, the provisions of this code, as applicable, shall take precedence over the provisions in the referenced code or standard”

## Slide 21: Certificate Section R401.3
Permanently posted on a wall in the space where the furnace is located, a utility room or an approved location inside the building
Don’t cover or obstruct the visibility of other required labels
Includes the following:
  R-values of insulation installed for the thermal building envelope, including ducts outside conditioned spaces
  U-factors and SHGC for fenestration
  Area-weighted U-factor and SHGC calculations
  Results from any required duct system and building envelope air leakage testing
  HVAC efficiencies and types
  SWH equipment
  If applicable, PV panel details
  If applicable, ERI score
  Code edition and compliance path
Notes:   The 2021 IECC requires a permanent certificate posted. The certificate shall be completed by the builder or other approved party. It should indicate the R-values of insulation installed for the building envelope, U-factors and SHGC for fenestration, results from any required duct system and building envelope air leakage testing, HVAC efficiencies, service water heating equipment, etc.

## Slide 22: Certificate, cont’d
  Certificate indicates “gas-fired unvented room heater”, “electric furnace”, or “baseboard electric heater”, rather than indicating an efficiency for those heating types

## Slide 23: Overview of Structure
Climate-Specific Requirements:
  Roofs
  Above grade walls
  Foundations
    Basements
    Slabs
    Crawlspaces
  Skylights, windows, and doors
  Solar Heat Gain Coefficient in warm climates
Non-climate Specific Requirements:
  Infiltration control
  Duct insulation, sealing & testing, no use of building cavities
  HVAC controls
  Piping Insulation and circulating service hot water requirements
  Equipment sizing
  Dampers
  Lighting
Notes: There are many other requirements not mentioned here: Mechanical ventilation, systems serving multiple dwelling units, snow melt and ice system controls, pools and spas...etc., the presentation will touch on all of these.

## Slide 24: Climate Zones
IECC Terminology
  "Climate Zone" has two components
    Nine temperature-oriented zones (0-8)
    Three named moisture regimes (moist, dry, marine)
    Theoretically 8x3=24 distinct zones, but only 15 occur in U.S.
  Two additional climate specifications influence requirements
    Warm-Humid line delineates counties that are warm-humid as defined by ASHRAE, with exceptions (affects only bsmt reqm'ts)
    The "Tropical Climate Zone" (not a separate zone) defines areas in which simplified/relaxed requirements apply under some conditions
Climate Zones in the U.S. are entirely geographical
  Defined along state/county lines
  International locations defined by local climate data (mean Temp, precipitation, humidity, etc.)

## Slide 25: Climate Zones for the 2021 IECC
Notes: The 2021 IECC updated the climate zones to be based on Standard 169-2013. New Climate Zone 0.

## Slide 26: Counties that are reassigned to warmer zones have generally less stringent code requirements
Updated Climate Zones
Red: Counties moving to warmer zones
Green: Counties moving to colder zones
Notes: About 2/3 of the states are affected by the reassignments in almost all climate zones, but most changes occur in counties in Climate Zones 4 and 5.

## Slide 27: Overview of Residential Code Requirements
Focus is on building envelope
  Ceilings, walls, windows, opaque doors, floors, foundations
  Sets insulation and fenestration levels, and solar heat gain coefficients
  Infiltration control - caulk and seal to prevent air leaks, and test
Ducts, air handlers, filter boxes – seal, insulate, and test
Limited space heating, air conditioning, and water heating requirements
  Federal law sets most equipment efficiency requirements, not the I-codes
No appliance requirements
Lighting equipment – 100% of lamps to be high-efficacy lighting sources
  Excluding kitchen appliance lighting fixtures
Notes: Limited HVAC requirements because Federal law preemptively regulates equipment efficiency itself, so it’s only the systems and related machinery that the code impacts.
A high-efficacy lamp is something like a compact fluorescent bulb.

## Slide 28: IECC Residential Compliance – 4 Pathway Options
ENERGY RATING INDEX (ERI)
U-factor (tradeoffs within individual components)
UA (tradeoffs between envelope components)
R-value (no tradeoffs)
Total Building Performance
R405
PRESCRIPTIVE
ERI
Compliance Alternative
R406
TOTAL BUILDING PERFORMANCE
TROPICAL CLIMATE REGION
R407
ADDITIONAL ENERGY EFFICIENCY R401.2.5
+ one option below
Notes: Compliance options:
Prescriptive
Total Building Performance
Energy Rating Index
Tropical Climate Region
The 2021 IECC removed use of the labels “prescriptive” and “mandatory” – now all requirements are identified within each path.
Additional Energy Efficiency requirements in R401.2.5 are applicable to all compliance paths.

## Slide 29: U-Factor and Total UA Alternative Section R402.1
U-factor
  Similar to Prescriptive R-Value but uses U-factors instead
    Allows for innovative or less common construction techniques such as structural insulated panels or advanced framing
    Allows no trade-offs between building components
Total UA Alternative
  Also uses U-factors in lieu of R-values, but allows trade-offs across all envelope components
    Primary approach used in REScheck software
    UA – U-factor x area of assembly
Notes: As a refresher…
U-factor table is for the entire assembly.
R-value table is only for the insulation.
UA Alternative – if the total bldg. thermal envelope UA (sum of U-factor x assembly area) is less than or equal to the total UA resulting from using the U-factor Table R402.1.4 (multiplied by the same area as in the proposed bldg.) the bldg. would be considered in compliance.
The SHGC requirements must be met in addition to UA compliance.
Note: Slabs are not part of UA approach because there is no Slab U in Table R402.1.2.

## Slide 30: Building Envelope Specific Requirements
Building Thermal Envelope consists of:
  Fenestration
  Ceilings
  Walls
    Above grade
    Below grade
    Mass walls
  Floors
  Slabs
  Crawl Spaces
Exceptions:
Low energy usage
< 3.4 Btu/h/sq.ft. OR
1 watt/sq.ft. of floor area OR
unconditioned spaces OR
log homes designed in accordance with ICC 400
Conditioned Space
attic
Notes: Most IECC requirements for residential buildings are for the Building Thermal Envelope as highlighted in orange on the diagram
The Building Thermal Envelope separates conditioned space from the outdoors and unconditioned spaces such as attics and garages
Fenestration is covered in this section.

## Slide 31: Ceilings without Attic Spaces Section R402.2.2 - (e.g., vaulted)
If insulation is full height uncompressed over exterior wall top plate
  R-30 allowed for up to 500 ft2 or 20% total insulated ceiling area, whichever is less, where
    Required insulation levels exceed R-30 in the interstitial space above a ceiling and below structural roof deck
    Design of roof/ceiling assembly does not provide sufficient amount of space to meet higher levels
Note: This reduction ONLY applies to the R-value prescriptive path, not the U-factor or Total UA alternatives
Notes: Typically vaulted ceiling or cathedral ceiling
If vaulted ceiling has a requirement of > R-30, but rafters or trusses can’t accommodate that, you can comply with not more than R-30 up to 500 sf or 20% of total insulated ceiling area, whichever is less.
Ex: If you have a small vaulted ceiling area over the entryway and because it’s small, it has relatively small framing members above and you’re in the North where R-38 is required, code will allow R-30. So, you don’t have to redesign the structure just to accommodate R-38 as long as the area is < 500 sf or 20% of ceiling area.

## Slide 32: Eave Baffle Section R402.2.3
For air permeable insulations in vented attics, a baffle shall be installed
Adjacent to soffit and eave vents
To maintain a net free area opening ≥ size of vent
To extend over top of attic insulation
May be of any solid material
Installed to the outer edge of exterior wall top plate
Where soffit venting isn’t continuous, baffles installed to prevent ventilation air in the eave soffit from bypassing the baffle

## Slide 33: Access Hatches and Doors Section R402.2.4
  Insulate to same R-value for wall or ceiling in Table 402.1.3
    e.g., required ceiling insulation = R-38, then attic hatch must be insulated to R-38
Exceptions:
Vertical doors that provide access can meet Table R402.1.3
Horizontal pull-down, stair-type access hatches separating conditioned from unconditioned spaces in CZ 0-4 – with additional restrictions

## Slide 34: Access Hatches and Door Insulation Installation and Retention Section R402.2.4.1
Weatherstrip and insulate vertical or horizontal access hatches and doors from conditioned spaces to unconditioned spaces (e.g., attics and crawl spaces)
Provide access to all equipment that prevents damaging or compressing the insulation
Install a wood framed or equivalent baffle or retainer or dam when loose fill insulation is installed
Notes: The baffle prevents the loose fill insulation from spilling into the living space when the attic access is opened and provides a permanent means of maintaining the installed R-value of the loose fill insulation. Foam board works well.
Ex: if you have an access hatch into an attic with R-38, the hatch itself has to be insulated to R-38 with a baffle or wall retainer to hold the loose fill insulation away from that opening when it’s opened.
Access to equipment example - You can’t just blow insulation all around the air handler, you have to build a platform up to the air handler that’s over the insulation.

## Slide 35: Steel-Frame Ceilings Section R402.2.6
Table R402.2.6 (PARTIAL TABLE) Steel-Frame Ceiling, Wall and Floor Insulation
(R-Value)
Table keys on the wood-frame requirement for the corresponding building component
R-13+R-5
R-13 + 4.2 or R-19 +2.1, or R-21 +2.8 or R-0+9.3 or R-15+R-3.8 or R-21 + 3.1
R-13
Steel Framed Wall
R-49 2x4, or 2x6, or 2x8, or 2x10
R-38
R-38 in 2x4, or 2x6, or 2x8
R-49 any framing
R-30
Steel Joist Ceilingsb
R-38 + 5
R-49
R-49 or R-38 + 3
R-38
R-38 or R-30 + 3 or R-26 + 5
R-30
Steel Truss Ceilingsb
Cold-Formed Steel
Equivalent R-valuea
Wood Frame R-value Requirement
R-0 + 15 or R-13 + 7.5 or R-15 + 7 or R-19 + 6
“R-X + R-Y” means R-X cavity plus R-Y continuous
In ceilings, insulation that exceeds the height of the framing must cover the framing

## Slide 36: Building Envelope Specific Requirements
Building Envelope consists of:
  Fenestration
  Ceilings
  Walls
    Above grade
    Below grade
    Mass walls
  Fenestration
  Floors
  Slabs
  Crawl Spaces
Conditioned Space
attic
Notes: Walls are covered in this section.

## Slide 37: Walls Covered by IECC
Exterior above-grade walls
Attic kneewalls
Skylight shaft walls
Perimeter joists
Basement walls
Garage walls (shared with conditioned space)

## Slide 38: Above Grade Walls
Insulate walls including those
next to unconditioned spaces
Don’t forget to insulate rim joists
Notes: Insulation should not be compressed behind the wiring or plumbing; this reduces the R-value of insulation.
Be sure the insulation has filled the entire cavity; batts that are cut too short will leave voids.
For continuous insulation make sure there are no voids and the insulation is well bonded to the outside framing.
Perimeter joists between floors must be insulated. Ex: 8 ft wall becomes a 9 ft wall.
While not a requirement, in some climates it is important to insulate exterior corners and on or in headers over doors and windows to eliminate heat transfer through the surfaces.

## Slide 39: Wood-Frame Walls Section R402
First value is cavity insulation, second is continuous insulation so. Therefore, as an example, “13+5” means R-13 cavity insulation plus R-5 continuous insulation
CLIMATE ZONE | … | WOOD FRAME WALL R-VALUE
0 |  | 13 or 0 + 10
1 |  | 13 or 0 + 10
2 |  | 13 or 0 + 10
3 |  | 20 or 13+5ci or 0+15
Table R402.1.3 (PARTIAL) INSULATION AND FENESTRATION REQUIREMENTS BY COMPONENT
Notes: Partial table shown

## Slide 40: Walls – Insulated Siding Section R303.1.4.1
R-value labeled on product package
Indicated on certification
Installer signature and date
Posted on site in conspicuous location
Thermal resistance (R-value) determined in accordance with ASTM C 1363

## Slide 41: Steel-Frame Walls Section R402.2.6
Table R402.2.6 Steel-Frame Ceiling, Wall and Floor Insulation
(R-Value)
R-13+R-5
R-13 + 4.2 or R-21 +2.8 or R-0+9.3 or R-15+R-3.8 or R-21 + 3.1
R-13
Steel Framed Wall
R-49 2x4, or 2x6, or 2x8, or 2x10
R-38
R-38 in 2x4, or 2x6, or 2x8
R-49 any framing
R-30
Steel Joist Ceilingsb
R-38 + 5
R-49
R-49 or R-38 + 3
R-38
R-38 or R-30 + 3 or R-26 + 5
R-30
Steel Truss Ceilingsb
Cold-Formed Steel
Equivalent R-valuea
Wood Frame R-value Requirement
R-0 + 15 or R-13 + 8 or R-15 + 8.5 or R-19 + 8 or R-21 + 7
“R-X + R-Y” means R-X cavity plus R-Y continuous
Table keys on the wood-frame requirement for the corresponding building component
Notes: Metal framing provides a more effective path for heat transmission than wood stud wall construction.
R-X+Y means RX cavity insulation plus R-Y continuous insulation (example R-26+5).
In ceilings, insulation that exceeds the height of the framing must cover the framing.
Steel framed assemblies shall meet the insulation requirements in Table R402.2.6 OR
the U-factor requirements in the U-factor Table R402.1.4 for Frame Walls and use a series-parallel path calculation method.

## Slide 42: Mass Walls Section R402.2.5
What type
  Concrete block, concrete, insulated concrete form (ICF), masonry cavity, brick (other than brick veneer), adobe, compressed earth block, rammed earth, solid timber, mass timber or solid logs
  Any other walls having a heat capacity >6 Btu/ft.2/ºF
Provisions
  Are assumed to be above grade walls
Notes: “Earth” includes adobe, compressed earth block, and rammed earth.
Mass walls have sufficient mass that they’re able to store a significant amount of heat in the all itself. Special requirements acknowledge that storage ability can improve the performance of the wall in terms of energy, especially in southern locations for cooling purposes.

## Slide 43: Mass Wall Requirements Section R402.2.5
Second (higher) number applies when more than half the R-value is on the interior of the mass (i.e., when the thermal mass is insulated from the conditioned space)
Table R402.1.3 INSULATION AND FENESTRATION REQUIREMENTS BY COMPONENT
Climate Zone | … | Mass Wall R-Value
0 |  | 3/4
1 |  | 3/4
2 |  | 4/6
3 |  | 8/13
4 except Marine |  | 8/13
5 and 4 Marine |  | 13/17
Notes: Partial table shown
Means that thermally massive walls lose a lot of their advantage when you insulate the building from them.
So, it’s much better from an energy standpoint to have insulation on the outside of a thermally massive wall than it is to have it on the inside. If you have most of the insulation on the inside, you have to have a little more of it.

## Slide 44: Building Envelope Specific Requirements
Building Envelope consists of:
  Fenestration
  Ceilings
  Walls
    Above grade
    Below grade
    Mass walls
  Floors
  Slabs
  Crawl Spaces
Conditioned Space
attic
Notes: Floors are covered in this section.

## Slide 45: Floors (Over Unconditioned Space) Section R402.2.7
CLIMATE ZONE | … | FLOOR R-VALUE
0 |  | 13
1 |  | 13
2 |  | 13
3 |  | 19
Table R402.1.3 (PARTIAL) INSULATION AND FENESTRATION REQUIREMENTS BY COMPONENT
Notes: Partial table shown

## Slide 46: Floors (Over Unconditioned Space) Section 402.2.7
Unconditioned space includes unheated basement, vented crawlspace, or outdoor air
Three options for floor cavity insulation:
1. Insulation must maintain permanent contact with underside of subfloor decking per manufacturer’s instructions to maintain required R-value or readily fill the available cavity space
2. Cavity insulation in contact with the top side of sheathing (insulation to extend from bottom of the top of all perimeter floor framing members and framing members to be air sealed
3. A combination of cavity and continuous insulation installed so cavity insulation is in contact with top side of continuous insulation that is installed on the underside of the floor framing. Combined R-value to equal required floor R-value. Insulation to extend from bottom to the top of all perimeter floor framing members and framing members to be air sealed.
Climate Zones | R-Value
0-2 | 13
3-4ab | 19
4c-6 | 30*
7-8 | 38*
Notes: Building Thermal Envelope: the basement walls, exterior walls, floor, roof, and any other building element that enclose conditioned space. This boundary also includes the boundary between conditioned space and any exempt or unconditioned space.
If insulation in the floor framing members doesn’t fill the cavity, the gap can’t be against the underside of the sub floor. Insulation must be pushed up to be in substantial contact with the sub floor and held by some means. This is to prevent airflow up above the insulation, which could short circuit its insulating ability.

## Slide 47: Steel-Frame Floors Section R402.2.6
Table R402.2.6 Steel-Frame Ceiling, Wall and Floor Insulation
(R-Value)
Table keys on the wood-frame requirement for the corresponding building component
“R-X + R-Y” means R-X cavity plus R-Y continuous
Wood Frame R-value Requirement
R-19 + 6 in 2x6, or R-19 + 12 in 2x8 or 2x10
R-19
R-19 in 2x6, or R-19 + 6 in 2x8 or 2x10
R-13
Steel Joist Floorb
Cold-Formed Steel-Frame
Equivalent R-valuea
Notes: Metal framing provides a more effective path for heat transmission than wood stud wall construction.
R-X+Y means R-X cavity insulation plus R-Y continuous insulation (example R-26+5).
Steel framed assemblies shall meet the insulation requirements in Table R402.2.6 OR
the U-factor requirements in the U-factor Table R402.1.4 for Frame Walls and use a series-parallel path calculation method.

## Slide 48: Defining Below-Grade Walls
Basement Wall – >50% below grade
Below grade
Basement wall
Exterior Wall –
<50% below grade
Notes: Define each wall individually.
If the grade is sloping, the average height of the grade of the wall should be used to determine whether it’s a below-grade or above-grade wall.
Back wall = below grade requirements
Front wall = above grade requirements
Side walls = could be either; best if plans specify where the backfill will go and how much of the wall will be buried.

## Slide 49: Basement Walls Section R402.2.8
≥ 50% below grade
Otherwise treat as above-grade wall
Insulated from top of basement wall down to 10 ft below grade or basement floor, whichever is less
Climate Zones | R-Value
0-2 | 0
3 | 5/13
4ab | 10/13
4c-8 | 15/19 or 13 + 5
“X/Y” means R-X continuous or R-Y cavity
15/19 requirement can be met with R-13 cavity (interior) plus R-5 continuous (exterior)
In zone 3, no insulation required in warm-humid counties (footnote f)
Notes: Where 50% or more of a wall assembly is below grade (based on exterior surface area), the below-grade wall requirement from the Envelope Requirements may be used for the entire assembly. Insulation R-values from Table R402 1.2 are considered full height of the basement wall.
Below-grade wall insulation must extend from the top of the basement down to 10 feet below grade or to the basement floor, whichever is less.
Walls associated with unconditioned basements must meet the requirements unless the floor above the basement is insulated accordingly.

## Slide 50: Building Envelope Specific Requirements
Building Envelope consists of:
  Fenestration
  Ceilings
  Walls
    Above grade
    Below grade
    Mass walls
  Floors
  Slabs
  Crawl Spaces
Conditioned Space
attic
Notes: Slabs are covered in this section.

## Slide 51: Slab Edge Insulation Section R402.2.9
Applies to slabs with a floor surface < 12 inches below grade
  R-10 insulation in Zones 4 and above
  Must extend downward from top of slab a minimum of 24” (Zones 3) or 48” (Zones 4-8)
  Insulation can be vertical or extend horizontally under the slab or out from the building
  Insulation extending outward must be under 10 inches of soil or pavement
    An additional R-5 is required for heated slabs
Figure 2
Flashing
Protection
Board
Rigid Insulation
Rigid Insulation
Slab
Rigid Insulation
Slab
Figure 4
Slab
Figure 3
Notes: Slab-edge insulation may be installed vertically or horizontally on the inside or outside of foundation walls. If installed vertically, it must extend downward from the top of the slab to the top of the footing. If installed horizontally, it must cover the slab edge and then extend horizontally (to the interior or exterior). Insulation extending outward must be under 10 inches of soil or protected by pavement.
Southern zones (0-2) = No requirement
CZ3 – need 2 ft of R-10
CZ 4 -8 – need 4 feet of R-10
A slab more than 12” below grade doesn’t require slab edge insulation, but the wall would be considered a below-grade wall.

## Slide 52
Slab Edge Insulation
Section R402.2.9
Rigid Insulation
Slab
Bevel Cut
Notes: The top edge of the insulation installed between the exterior wall and the edge of the interior slab can be cut at a 45 degree angle away from the exterior wall.
This is an example of insulation cut at a 45-degree bevel cut this is a way to avoid bringing the insulation to the top of the slab edge so a carpet tack strip can be attached.
Insulation is not required where the code official deems termite infestation to be very heavy.

## Slide 53: Building Envelope Specific Requirements
Building Envelope consists of:
  Fenestration
  Ceilings
  Walls
    Above grade
    Below grade
    Mass walls
  Floors
  Slabs
  Crawl Spaces
Conditioned Space
attic
Notes: Crawlspaces are covered in this section.

## Slide 54: Crawl Space Wall Insulation Section R402.2.10
Implies an unvented crawlspace (aka, conditioned crawlspace)
  Space must be mechanically vented or receive minimal supply air (Refer to IRC)
  Exposed earth must be covered with a continuous Class I vapor retarder
Notes: The code requires the crawl space wall insulation be permanently fastened to the wall and extend downward from the floor to the finished grade level and then vertically and/or horizontally for not less than an additional 24”.
However, there are some criteria that must be met in order to use this insulation method:
The crawlspace may not have ventilation openings that communicate directly with outside air
The crawlspace floors must be covered with vapor retarder, the joints must overlap 6” and be sealed or taped. The edges should extend at least 6” up the stem wall and be attached to the stem wall.
The crawlspace must have openings back to conditioned space.
The crawlspace floor must be covered with an approved vapor retarder material, the joints must overlap 6” and be sealed, the edges should extend at least 6” up the stem wall and attached to the stem wall.
The IRC allows the construction of unventilated crawlspaces. To meet the requirements the crawlspace walls must be insulated to the R-value specified in the energy code. The crawlspace must either be provided with conditioned air or with mechanical ventilation. The code does not specify the quantity of conditioned air to supply the crawlspace.
If mechanical ventilation is selected, the crawlspace must be ventilated at 1 CFM per 50 square feet. The ground surface must also be covered with an approved vapor retarder material. To eliminate moisture from the crawlspace the sill plate and perimeter joist must be sealed. Also, while not a code requirement, all joints in the vapor retarder should be overlapped and taped. This includes the connection between the vapor retarder and crawlspace wall.

## Slide 55: Vented & Unvented Crawlspaces Section R402.2.10
Vented Crawlspace Requirements:
The raised floor over the crawlspace must be insulated.
A vapor retarder may be required as part of the floor assembly.
Ventilation openings must exist that are equal to at least 1 square foot for each 150 square feet of crawlspace area and be placed to provide cross-flow (IRC 408.1, may be less if ground vapor retarder is installed).
Ducts in crawlspace must be sealed and have R-6 insulation.
Unvented Crawlspace Requirements:
The crawlspace ground surface must be covered with an approved vapor retarder (e.g., plastic sheeting).
Crawlspace walls must be insulated to the R-value requirements specific for crawlspace walls (IECC Table R402.1.2).
Crawlspace wall insulation must extend from the top of the wall to the inside finished grade and then 24” vertically or horizontally.
Crawlspaces must be mechanically vented (1 cfm exhaust per 50 square feet) or conditioned (heated and cooled as part of the building envelope).
Ducts are inside conditioned space and therefore don’t need to be insulated.
Notes: These are some other requirements that might pertain to the crawlspace whether it is vented or unvented. Not all of these requirements are addressed in the IECC and come from other codes such as the IRC.
Typical vented CS will have insulation on the floor over the CS, whereas unvented CS will have insulation on CS walls.
Vented CS may be required to have vapor retarder as part of floor assembly, whereas unvented will be required to have vapor retarder on ground surface underneath.
Vented CS has requirements for the openings; unvented CS must be mechanically vented one way or other, either with pure exhaust or actually bringing conditioned air in.
Ducts in vented CS must be insulated to R-6 because they’re in unconditioned space.

## Slide 56: Mass Walls Section R402.2.5 - U-Factor
Provisions
  Apply when wall heat capacity > 6 Btu/ft2/ºF
  When more than half the insulation is on the interior, the mass wall U-factors can’t exceed values listed in Table R402.1.2, footnote b (Partial Table below)
Climate Zones | U-Factor Maximum
0-1 | 0.197 / 0.170
2 | 0.165 / 0.140
3 | 0.098 / 0.120
4 except Marine | 0.098 / 0.087
Notes: The second set of values in the table on this slide come from footnote b in Table R402.1.2.
The second U-factor in the table is for interior insulated walls

## Slide 57: Fenestration Trade-off Limits Section R402.5
Hard limits on U-factor in northern U.S. (cannot be exceeded, even in trade-offs or ERI path)
  U-0.75 for skylights in Zones 4-8
  U-factors of individual windows or skylights can be higher if area-weighted average is below these limits.
Climate Zones | U-Factor Maximum
4-5 | 0.48
6-8 | 0.40
Notes: U-Factor is a measure of how well the assembly conducts heat. The lower the number, the better the assembly acts as an insulator.
A window U-factor is based on the interior surface area of the entire assembly, including glazing, sash, curbing, and other framing elements. Center-of-glass U-factors cannot be used.
The code requires windows, glass doors, and skylights to be rated by the National Fenestration Rating Council and to have labels that show the rated U-factor and SHGC values for the glazing unit, but allows default values from Table R303.1.3).

## Slide 58: Fenestration Trade-off Limits, cont’d
Hard limit on Solar Heat Gain Coefficient in southern U.S. (Zones 0-3)
    SHGC cannot exceed 0.40, even in performance trade-offs or ERI path
    SHGCs of individual windows or skylights can be higher if area-weighted average is below this limit.
  Exception: Maximum U-factor and SHGC not required in storm shelters complying with ICC 500
Solar Heat Gain Coefficient
Notes: SHGC is a measure of how much solar gain is transmitted through the window by solar radiation.
The lower the SHGC value of a window the less sunlight and heat can pass through the glazing.
These are based on building average; SHGC of individual windows or skylights can be higher if area-weighted average is below this limit.
In locations in climate zones 0-3, the combined SHGC (the area weighted average) of all glazed fenestration products in the building shall not exceed .40. Under no circumstances can the area-weighted average SHGC exceed 0.40 in zones 0-3, regardless of what trade-offs are used.

## Slide 59: Sunrooms
Less stringent insulation R-value and glazing U-factor requirements
Sunroom definition:
  One story structure
  Glazing area >40% glazing of gross exterior wall and roof area
  Separate heating or cooling system or zone
  Must be thermally isolated (both HVAC and physical separation—closeable doors or windows between sunroom and rest of the house)
  Can always meet Table R402.1.2 requirements with unlimited glass
Notes:   Sunroom: a one-story structure attached to a dwelling with a glazing area in excess of 40 percent of the gross area of the structure’s exterior walls and roof.
  REScheck cannot be used for Sunroom compliance.
  Patio and enclosure folks came up with this because cannot meet the R-value requirements. Code has “relaxed” requirements for sunrooms if certain things are true: must have separate heating or cooling system or be zoned as a separate zone and must be thermally isolated (needs to have closeable doors on windows or doors between it and the rest of the house).

## Slide 60: Sunroom and Heated Garage Requirements Section R402.2.12 / R402.3.5
Ceiling Insulation
  Zones 0-4 R-19
  Zones 5-8 R-24
Wall Insulation
  All zones R-13
Fenestration U-Factor
  Zones 2-8 0.45
Skylight U-Factor
  Zones 2-8 0.70
Notes: New wall(s), windows and doors separating a sunroom or heated garage from conditioned space to meet the building thermal envelope requirements.
These are prescriptive requirements and the SHGC requirements are still applicable and not less stringent, regardless of whether it is a sunroom or not.

## Slide 61: Air Leakage Section R402.4
Floor
Window
Attic Hatch
Foundation
Chimney
Plumbing
Wiring
Exterior
Door
Lights
Ceiling
Penetrations
Building thermal envelope (Section R402.4.1)
Recessed lighting
Fenestration
Fireplaces
Rooms with fuel-burning appliances
Electrical and communication outlet boxes

## Slide 62: Air Leakage Section R402.4
Building thermal envelope
Notes: The sealing methods between dissimilar materials shall allow for differential expansion and contraction.

## Slide 63: Building Thermal Envelope Section R402.4.1 – Air Leakage
Requires BOTH:
  Whole-house pressure test – maximum air leakage under any compliance path to not exceed 5 ACH or 0.28 CFM/ft2 of dwelling unit enclosure area
  When complying per prescriptive path:
    Testing may occur any time after creation of all building envelope penetrations
  Field verification of items listed in Table R402.4.1.1
Air Leakage Rate | Climate Zone | Test Pressure
≤ 5 ACH | 0-2 | 50 Pascals
≤ 3 ACH | 3-8 | 50 Pascals
Notes: Two options: whole house pressure test with a blower door system to make sure that the envelope leakage isn’t more than what’s expected OR use a fairly thorough checklist from the code
Whole-house pressure test section includes instructions for setting up. For example: Exterior windows and doors, fireplace and stove doors to be closed but not sealed.
Field verification states that the code official can require an approved party, independent from the insulation installer, inspect the air barrier and insulation.

## Slide 64: Table R402.4.1.1
Component | Air Barrier Criteria | Insulation Installation Criteria
General requirements | A continuous air barrier shall be installed in the building envelope. Breaks or joints in the air barrier shall be sealed. | Air-permeable insulation shall not be used as a sealing material.
Ceiling/attic | The air barrier in any dropped ceiling or soffit shall be aligned with the insulation and any gaps in the air barrier sealed. Access openings, drop down stair or knee wall doors to unconditioned attic spaces shall be sealed. | The insulation in any dropped ceiling/soffit shall be aligned with the air barrier.
Walls | The junction of the foundation and sill plate shall be sealed. The junction of the top plate and the top of exterior walls shall be sealed. Knee walls shall be sealed. | Cavities within corners and headers of frame walls shall be insulated by completely filling the cavity with a material having a thermal resistance R-value of not less than R-3 per inch. Exterior thermal envelope insulation for framed walls shall be installed in substantial contact and continuous alignment with the air barrier.
Windows, skylights and doors | The space between framing and skylights and the jambs of windows and doors shall be sealed. | 
(partial table)
Notes: This is only a part of Table R402.4.1.1

## Slide 65: Building Thermal Envelope Section R402.4.1.3 – Leakage Rate
Prescriptive
Total Building Performance and ERI – R402.4.1.2 sets a 5.0 ACH50 trade-off limit on tested air leakage for any climate zone
Air Leakage Rate | Climate Zone | Test Pressure
≤ 5 ACH | 0-2 | 50 Pascals
≤ 3 ACH | 3-8 | 50 Pascals
Air Leakage Rate | Climate Zone | Test Pressure
≤ 5 ACH | 0-2 | 50 Pascals
≤ 5 ACH | 3-8 | 50 Pascals

## Slide 66: Fireplaces Section R402.4.2
New wood-burning fireplaces shall have tight fitting flue dampers or doors, and outdoor combustion air
Tight fitting doors on fireplaces that are:
  Factory built – listed and labeled per UL 127

## Slide 67: Fenestration Air Leakage Section R402.4.3
  Exceptions
    Site-built windows, skylights, and doors
TYPE | AIR INFILTRATION RATE
Windows, sliding glass doors, and skylights | 0.3 cfm/ft2
Swinging doors | 0.5 cfm/ft2
Notes: Tested to NFRC 400 or AAMA/WDMA/CSA 101/ 1.S.2/A440

## Slide 68: Rooms Containing Fuel Burning Appliances Section R402.4.4
Climate Zones 3-8
Open combustion fuel burning appliances where open combustion air ducts provide combustion air
  The appliances and combustion air opening shall be located outside the building thermal envelope OR
  Enclosed in a room isolated from inside the thermal envelope
    Sealed and insulated per Table R402.1.3
    Door gasketed and sealed
    Any ducts or water lines insulated per R403
  Combustion air duct insulated to an R-value of not less than R-8 where it passes through conditioned space
  Exceptions:
    Direct vent appliances with both intake and exhaust pipes installed continuous to outside
    Fireplaces and stoves complying with R402.4.2 and Section R1006-IRC
Notes: Rooms insulated per Table R402.1.2 where the walls, floors, and ceilings shall meet not less than the basement wall R-value requirement

## Slide 69: Recessed Lighting Fixtures Section R402.4.5
Type IC rated and labeled as meeting ASTM E 283 when tested at 1.57 psf (75 Pa) pressure differential with no more than 2.0 cfm of air movement
Sealed with a gasket or caulk between the housing and interior wall or ceiling covering
Notes: When installed in the building envelope, recessed lighting fixtures shall meet one of these requirements.
IC means “insulation contact.” Another designation label you might encounter is Air-Lok.
Type IC rated in accordance with ASTM E 283 admitting no more than 2.0 cfm of air movement from the conditioned space to the ceiling cavity.

## Slide 70: Electrical and Communication Outlet Boxes Section R402.4.6
Sealed to limit air leakage between conditioned and unconditioned spaces
Tested per NEMA OS 4, at 1.57 psf (75 Pa) pressure differential with no more than 2.0 cfm of air movement
Boxes marked either NEMA OS 4 or OS 4
Installed per manufacturer’s instructions

## Slide 71: Mechanical Systems & Equipment
Minimum equipment efficiency set by Federal law, not the I-Codes
Notes: Not really dealt with directly in the IECC because Federal law establishes minimum efficiencies and those Federal requirements preempt any state or local building codes.

## Slide 72: Requirements for Systems Section R403
Controls
Heat pump supplementary heat
Hot water boiler outdoor temperature setback
Ducts
HVAC piping insulation
Hot water systems
Ventilation
  Dampers
Equipment sizing
Systems serving multiple dwelling units
Snow melt controls
Energy consumption of pools and spas

## Slide 73: Programmable Thermostat Section R403.1.1 - Controls
  At least one programmable thermostat controlling the primary heating/cooling per dwelling unit
  Capability to set back or temporarily operate the system to maintain zone temperatures
      Not less than 55ºF (13ºC) or
      Not greater than 85ºF (29ºC)
  Initially programmed by manufacturer with:
      heating temperature set point not greater than 70ºF (21ºC) and
      cooling temperature set point not less than 78ºF (26ºC)
Notes: Programmable thermostat capable of controlling the heating and cooling system on a daily schedule to maintain different set points at different times of the day and different days of the week.

## Slide 74: Heat Pump Supplementary Heat Section R403.1.2 - Controls
Prevent supplementary electric-resistance heat when heat pump can meet the heating load
Exception
  During defrost
Notes: Heat pumps having supplementary electric resistance heat to have controls that except during defrost, prevent supplemental heat operation when the heat pump compressor can meet the heating load.

## Slide 75: Hot Water Boiler Temperature Reset Section R403.2
Manufacturer to equip each boiler (gas, oil and electric) with a means to automatically adjust water temperature supplied by boiler to ensure incremental change of the inferred head load will cause an incremental change in the temperature of the water supplied by the boiler
  Outdoor reset OR
  Indoor reset OR
  Water temperature sensing
Not required for boilers equipped with tankless domestic water heating coil

## Slide 76: Ducts Located Outside Conditioned Space Section R403.3.1
Supply and return ducts in attics: R-8 where > 3” diameter, R-6 if < 3”
Ducts buried beneath a building – insulated as required per this section or have equivalent thermal distribution efficiency
  Underground ducts using thermal distribution efficiency method to be listed and labeled with R-value equivalency

## Slide 77: Ducts Located in Conditioned Space Section R403.3.2
For simulated performance path, buried ducts may be considered inside conditioned space if:
The duct system is actually located completely within the continuous air barrier and within the building thermal envelope, OR
The ducts are buried within ceiling insulation in accordance with Section R403.3.6 and all of the following conditions exist:
  2.1. The air handler is located completely within the continuous air barrier and within the building thermal envelope.
  2.2. The duct leakage, as measured either by a rough-in test of the ducts or a post-construction total system leakage test to outside the building thermal envelope in accordance with Section R403.3.4, is less than or equal to 1.5 cubic feet per minute (42.5 L/min) per 100 square feet (9.29 m2) of conditioned floor area served by the duct system.
  2.3. The ceiling insulation R-value installed against and above the insulated duct is greater than or equal to the proposed ceiling insulation R-value, less the R-value of the insulation on the duct.

## Slide 78: Ducts Buried within Ceiling Insulation
Define buried-duct practices that are explicitly allowed
Provide a means to characterize the performance of a buried duct system as an equivalent duct insulation R-value
Allow simplified credit for buried ducts in the performance path
  Buried duct system may be considered inside conditioned space if certain requirements are met
Prior to 2018, the IECC did not prohibit buried ducts, but neither did it define the practice or make specific allowance for it. Provisions:

## Slide 79: Ducts Buried within Ceiling Insulation Section R403.3.3
Where supply and return air ducts are partially or completely buried in ceiling insulation, such ducts shall comply with all of the following:
  1. The supply and return ducts shall have an insulation R-value not less than R-8.
  2. At all points along each duct, the sum of the ceiling insulation R-value against and above the top of the duct, and against and below the bottom of the duct, shall be not less than R-19, excluding the R-value of the duct insulation.
  3. In Climate Zones 0A, 1A, 2A and 3A, the supply ducts shall be completely buried within ceiling insulation, insulated to an R-value of not less than R-13 and in compliance with the vapor retarder requirements of Section 604.11 of the International Mechanical Code or Section M1601.4.6 of the International Residential Code, as applicable.
Exception: Sections of the supply duct that are less than 3 feet (914 mm) from the supply outlet shall not be required to comply with these requirements.

## Slide 80: Effective R-value of Deeply Buried Ducts Section R403.3.3.1
Where using a simulated energy performance analysis, sections of ducts that are:
  installed in accordance with Section R403.3.3
  located directly on, or within 5.5 inches (140 mm) of the ceiling
  surrounded with blown-in attic insulation having an R-value of R-30 or greater
  located such that the top of the duct is not less than 3.5 inches below the top of the insulation
shall be considered as having an effective duct insulation R-value of R-25

## Slide 81: Duct Sealing Section R403.3.4
Sealing
  Joints and seams to comply with IMC or IRC
  All ducts, air handlers, and filter boxes to be sealed

## Slide 82: Sealed Air Handler Section R403.3.4.1
Air handlers to have a manufacturer’s designation for an air leakage of ≤ 2% of design air flow rate per ASHRAE 193

## Slide 83: Duct Testing Section R403.3.5
Ducts shall be pressure tested per ANSI/RESNET/ICC 380 or ASTM E1554 to determine air leakage by either of the following:
  Rough-in test
    Total leakage measured with a pressure differential of 0.1 inch w.g. (25 Pa) across the system including manufacturer’s air handler enclosure
      All registers taped or otherwise sealed
  Postconstruction test
    Total leakage measured with a pressure differential of 0.1 inch w.g. (25 Pa) across the entire system including manufacturer’s air handler enclosure
      All registers taped or otherwise sealed
  Exception
    Test not required for ducts serving heat or energy recovery ventilators not integrated with ducts serving heating or cooling systems
    (Note: exception for ducts in conditioned space was removed)

## Slide 84: Duct Leakage Section R403.3.6
Total leakage of ducts, where measured in accordance with Section 403.3.5 shall be as follows:
  Rough-in test
    Total leakage ≤4 cfm/per 100 ft2 of conditioned floor area
      if air handler not installed at time of test
        Total air leakage ≤3 cfm/per 100 ft2
  Postconstruction test
    Total leakage ≤4 cfm/per 100 ft2 of conditioned floor area
  Test for ducts within thermal envelope
    Total leakage ≤8 cfm/per 100 ft2 of conditioned floor area

## Slide 85: Duct Tightness Tests

## Slide 86: Building Cavities Section R403.3.7
Framing cavities cannot be used as ducts or plenums

## Slide 87: Mechanical System Piping Insulation Section R403.4
R-3 required on
  HVAC systems
    Exception: Piping that conveys fluids between 55 and 105°F
If exposed to weather,
  protect from damage, including
    Sunlight
    Moisture
    Equipment maintenance
    Wind
  Provide shielding from solar radiation that can cause degradation of material
  Adhesive tape is not allowed

## Slide 88: Service Hot Water Systems Section R403.5
Heated water circulation systems
Demand recirculation water systems
Heat trace systems

## Slide 89: Heated Water Circulation and Temp. Maintenance Systems Section R403.5.1
Heated water circulation systems
  provided with circulation pump
  return pipe must be a dedicated return pipe or a cold water supply pipe
  gravity and thermosyphon circulation systems are prohibited
Controls shall
  start the pump based on identification of the demand for hot water within the occupancy
  automatically turn off pump when water in the loop is at desired temperature and there is no demand for hot water
  limit the temperature of water entering cold water pipe to not greater than 104ºF
Automatic controls, temperature sensors, and pumps shall be accessible
Manual controls shall be readily accessible

## Slide 90: Demand Recirculation Water Systems Section R403.5.1.1
Demand recirculation water system to have controls that
  start pump upon:
    receiving a signal from action of user of a fixture or appliance
    sensing the presence of a user of a fixture or
    sensing the flow of hot or tempered water to a fixture fitting or appliance

## Slide 91: Heat Trace Systems Section R403.5.1.2
Electric heat trace systems shall comply with IEEE 515.1 or UL 515
Controls shall automatically adjust the energy input to the heat tracing to maintain the desired water temperature in the piping in accordance with the times when heated water is used in the occupancy

## Slide 92: Hot Water Pipe Insulation Section R403.5.2
R-3 required on
  Piping ≥ ¾ in. nominal diameter inside conditioned space
  Piping serving more than one dwelling unit
  Piping located outside the conditioned space
  Piping from the water heater to a distribution manifold
  Piping under a floor slab
  Buried piping
  Supply and return piping in recirculating systems other than demand recirculation systems
Image courtesy of Ken Baker, K energy
Notes: Note that all > or equal to ¾-inch piping must be insulated.

## Slide 93: Drain Water Heat Recovery Units Section R403.5.3
Comply with CSA B55.2 and tested in accordance with CSA B55.1
Portable water-side pressure loss of drain water hat recovery units shall be < 3 psi for individual units connected to 1 or 2 showers
  < 2 psi if connected to > 3 showers

## Slide 94: Mechanical Ventilation Section R403.6
Ventilation
  Building and dwelling units to have ventilation complying with IRC or IMC or with other approved means
  Outdoor air intakes and exhausts shall have automatic or gravity dampers that close when the ventilation system is not operating
Heat or energy recovery ventilation
  Dwelling units provide HRV or ERV in Climate Zones 7-8
  System balanced with minimum sensible heat recovery efficiency of 65% at 32F at a flow ≥ design airflow
Whole-dwelling mechanical ventilation system fans to meet efficacy in Table R403.6.2
  Fans tested per HVI 916 and listed
  Airflow reported in product listing or on label
  Fan efficacy
    reported in product listing or derived from input power and airflow values reported in product listing or on label
    For fully ducted HRV, ERC, balanced and in-line fans to be determined at static pressure not less than 0.2” w.c.
    For ducted range hoods, bathroom and utility room fans to be determined at static pressure not less than 0.1” w.c.

## Slide 95: Mechanical Ventilation Section R403.6 Cont’d
Tested and verified to provide minimum ventilation flow rates per R403.6
Testing performed
  per manufacturer’s instructions OR
  Using flow hood or box, flow grid, or other airflow measuring device at the fan’s inlet terminals or grilles, outlet terminals or grilles, or in connected ventilation ducts
Where required by code official, testing to be conducted by an approved third party, with a signed, written report with results provided to code official

## Slide 96: Equipment Sizing and Efficiency Rating Section R403.7
Equipment Sizing
  Load calculations determine the proper capacity (size) of equipment
    Goal is big enough to ensure comfort but no bigger
  Sizing shall be performed in accordance with ACCA Manual S based on loads calculated in accordance with ACCA Manual J (other approved methods)
Efficiency Rating
  New or replacement heating/cooling equipment shall have an efficacy rating equal to or greater than minimum required by federal law for geographic location of installation
Notes: Equipment sizing is a direct reference to the IRC. Intent is to get the HVAC system sized correctly so it operates as efficiently as possible.
Oversized equipment has a higher initial cost, a higher operating cost, may provide less comfort, and the short-cycling reduces the equipment life expectancy. Any one of these is a good reason not to oversize.
Heating and cooling system design loads for the purpose of sizing systems and equipment shall be determined in accordance with the procedures described in the ACCA Manual J or an equivalent computation procedure.

## Slide 97: Systems Section R403.8
Systems serving multiple dwelling units shall comply with Sections C403 and C404 instead of Section R403
Notes: Section C403: Building Mechanical Systems
Section C404: Service Water Heating
Metering – separate metering

## Slide 98: Snow Melt System Controls Section R403.9
Snow- and ice-melting system controls
  Automatic shutoff when pavement temperature is > 50F and precipitation is not falling
  Automatic or manual shutoff when outdoor temperature is > 40F
Notes: Requirements apply when systems are supplied through energy service to the building.

## Slide 99: Energy Consumption of Pools and Spas Section R403.10
Heaters
  with a readily accessible on-off switch that is integral
  part of heater mounted on the exterior of heater or
  external to within 3 feet of heater
  Switch shall not change the setting of heater thermostat
  Switches shall be in addition to the circuit breaker for the power to the heater
  fired by natural gas not allowed to have continuously burning pilot lights
Time switches (or other control method) to automatically turn heaters and pumps off and on according to a preset schedule installed on all heaters and pump motors
Note: heaters, pumps, and motors with built-in timers meet the requirement
  Exceptions
    Public health standards requiring 24-hour pump operation
    Pumps operating pools with solar and waste-heat recovery heating systems

## Slide 100: Covers Section R403.10.3
On outdoor heated pools and outdoor permanently installed spas
  Vapor-retardant cover OR
  Other approved vapor retarder means
  Exception:
  If >75% of energy from heat pump or on-site renewable energy system (computed over an operation season not fewer than 3 calendar months)
Notes: Requirement for cover to be left with the pool at time of construction. Covers required for all heated pools and inground permanently installed spas.
Limiting the evaporation of water is very important in terms of avoiding energy loss.
Exception is computed over an operation season of not less than three calendar months.

## Slide 101: Portable Spas Section R403.11
Energy consumption of electric-powered portable spas shall be controlled by the requirements of APSP14

## Slide 102: Lighting Equipment Section R404.1
All permanently installed lighting fixtures shall contain only high efficacy lighting sources
Exception: kitchen appliance lighting fixtures
Notes: High efficacy light sources: compact fluorescent lamps, LED lamps, T-8 or smaller diameter linear fluorescent lamps, or other lamps with a minimum efficacy of not less than 65 lumens per watt or luminaires with efficacy of not less than 45 lumens per watt

## Slide 103: Exterior Lighting Section R404.1.1
Connected exterior lighting to comply with Section C405.4
Exceptions:
Detached one- and two-family dwellings
Townhouses
Solar-powered lamps not connected to any electric service
Luminaires controlled by a motion sensor
Lamps and luminaires that comply with Section R404.1
Notes: New in 2021 IECC – for low-rise (3 stories and less) multifamily buildings

## Slide 104: Fuel Gas Lighting Equipment Section R404.1.2
Fuel gas lighting systems may not have continuously burning pilot lights

## Slide 105: Interior Lighting Controls Section R404.2
Permanently installed fixtures to be controlled with a dimmer, an occupant sensor control or other control installed or built into the fixture
Exceptions:
Bathrooms
Hallways
Exterior lighting fixtures
Lighting designed for safety or security

## Slide 106: Exterior Lighting Controls Section R404.3
Where total permanently installed exterior lighting power is > 30 watts
Lighting to be controlled by manual on and off switch which permits automatic shut-off actions (not required for dwelling units)
Lighting to be automatically shut off when daylight is present and satisfies the lighting needs
Controls that override automatic shut-off actions not allowed unless override automatically returns control to normal operation within 24 hrs

## Slide 107: Total Building Performance Section R405
Proposed design to be shown to have an annual energy cost that is less than or equal to the annual energy cost of the standard reference design
Specifications for standard reference and proposed design are in Table R405.4.2(1)
  New in 2018: Allowance for batch sampling of stacked multifamily units

## Slide 108: Total Building Performance, cont’d
Requires computer software with specified capabilities (local official may approve other tools)
Includes both envelope and some systems
  Equipment treated equally in standard and proposed design
Allows greatest flexibility
  Can trade off tight duct systems
Defines compliance based on equivalency of calculated energy cost or source energy
Section R405 specifies “ground rules”
  These will generally be “hidden” in compliance software calculation algorithms
  Similar ground rules are used in home federal tax credits and ENERGY STAR Home guidelines
Notes: The simulated performance alternative can be used for building designs that do not comply with all the prescriptive requirements in Chapter 4 [RE] of the IECC. Under the simulated performance alternative, a “Proposed design” will comply with the code if the calculated annual energy cost is not greater than a similar building (the “Standard design”) designed in accordance with Chapter 4 [RE].
The Proposed design uses the same energy sources, floor area, geometry, design conditions, occupancy, climate data, and usage schedule as the Standard design. Some energy-conserving strategies to improve the performance of the Proposed design include exterior shading of windows, passive solar design, thermal mass heat storage, improved thermal envelope, improved duct systems, reduced air infiltration, and high-efficiency heating, cooling, and water heating equipment.
Some cost associated with this as specialized software must be used. Code officials and others must be able to read resulting reports.

## Slide 109
Service Hot Water Changes Section R405.4 – Calculation Procedure - Hot Water Distribution Compactness Factor
Locate the water heater and the hot water fixtures and appliances
Draw a rectangle through the center line of the water heater and the plumbing walls next to the hot water fixtures and appliances
Calculate the area of this rectangle
Divide this area by the conditioned floor area of the home to get the Compactness Ratio
Determine if a credit can be taken and how large it can be

## Slide 110: Energy Rating Index Section R406
First included in the 2015 IECC, ERI path differs from the traditional prescriptive and performance paths
  Unlike the performance path, is not based on the prescriptive requirements
  Fundamental requirement is a single rating (ERI) based on RESNET/ICC 301
Requirements table R406.2 lists requirements to be met

## Slide 111: Energy Rating Index Section R406
Compliance with this method must be completed by an approved third party and documentation including compliance reports must be reviewed by the code official
Compliance is demonstrated if the calculated ERI is ≤ a defined threshold for the climate zone in which the building is located
Summary of 2021 IECC Changes
  Required values in Table R406.5 were reduced
  R406.3 limits renewable energy production to reduce no more than 5% of total energy use
  Additional Efficiency Package Options – requires a target score reduction of 5%
Notes: ERI -

## Slide 112: Energy Rating Index Section R406
Climate Zone | ERIa
0-1 | 52
2 | 52
3 | 51
4 | 54
5 | 55
6 | 54
7 | 53
8 | 53
Table R406.5
Maximum Energy Rating Index

## Slide 113
Building Thermal Envelope Section R406.3
ERI envelope backstop at 115% of 2021 IECC Reference UA
On-site renewables are NOT included:
Proposed total building thermal envelope UA (sum of U-factor x assembly area) to be less than or equal to building thermal envelope UA using prescriptive U-factors from Table R402.1.2 x 1.15 (Equation 4-1).
Area-weighted maximum fenestration SHGC permitted in Climate Zones 0-3 to be 0.30.
ERI envelope backstop to 2018 IECC with on-site renewable energy
Building thermal envelope to be greater than or equal to levels of efficiency and SHGC in Table R402.1.2 or Table R402.1.4 of the 2018 IECC
Notes: Note: there was an errata issued to use correct reference of 2018 IECC for second bullet
2018 IECC had 2009 IECC as envelope backstop

## Slide 114: Energy Rating Index Section R406.4
ERI is determined in accordance with ANSI/RESNET/ICC 301
Except for buildings covered by IRC, the ERI Reference Design Ventilation rate to be in accordance with Equation 4-2:
Equation 4-2
Ventilation rate, CFM = (0.01 x total square foot area of house) + [7.5 x (number of bedrooms + 1)]
Energy used to recharge or refuel a vehicle used for transportation on roads not on the building site not included in ERI reference design or rated design
Notes: For compliance, any reduction in energy use of rated design associated with on-site renewable energy to not exceed 5% of total energy use

## Slide 115: Tropical Zone Section R407
Buildings deemed to comply at elevation < 2,400 feet above sea level where the following conditions are met:
  < ½ space is air conditioned
  Occupied space is not heated
  > 80% solar, wind, or other renewable energy source supplies service water heating
  SHGC on fenestration < 0.40 or overhang projection factor > 0.30
  Lighting in accordance with R404
  Exterior roof complies with Table C402.2.11 (commercial cool roof) or insulation of > R-15, if present, attics above insulation are vented and attics below insulation unvented
  Roof surface slope of not less than ¼ unit vertical in 12 units horizontal (i.e., 1/48 or 2.1% [note: code says 21%])
Notes: Minimum roof slope requirement did not change between 2015 and 2018, but the text was "clarified," and in the process an error/ambiguity inserted.

## Slide 116: Tropical Zone Section R407.2 Cont’d
  Operable fenestration provides ventilation of not less than 14% of floor area for each room or equivalent ventilation is provided by a ventilation fan
  Bedrooms with 2 exterior walls facing different directions have operable fenestration
  Interior doors to bedrooms capable of being secured open
  Ceiling fan or rough-in provided for bedrooms and the largest space that is not used as a bedroom

## Slide 117
Additional Efficiency Package Options Section R408
R408.2.1 – Enhanced envelope performance option
  Design UA <= Standard UA * 0.95
R408.2.2 – More efficient HVAC equipment performance option
  Furnace >= 95 AFUE and AC >= 16 SEER
  Air Source Heat Pump >= 10 HSPF/16 SEER
  Ground Source Heat Pump >= 3.5 COP
R408.2.3 – Reduced energy use in service water heating option
  Fossil fuel water heater >= 0.82 EF
  Electric water heater >= 2.0 EF
  Solar water heater >= 0.4 Solar Fraction
R408.2.4 – More efficient duct thermal distribution system option
  100% of ducts and air handler inside building thermal envelope
  100% of ductless or hydronic system inside building thermal envelope
  100% of duct thermal distribution system located in conditioned space
R408.2.5 – Improved air sealing and efficient ventilation system option
  Air Leakage <= 3.0 ACH50
  HRV (75% Sensible Recovery Efficiency) or ERV (50% Latent Recovery/Moisture Transfer)

## Slide 118: Existing Buildings Section R501 - General
Additions, alterations, or repairs
Existing buildings
Maintenance
Compliance
New and replacement materials
Buildings designated as historic
Notes: Buildings designated as historic
  National/state/local historical register
  Some jurisdictions may still require additions to these structures to comply with the energy code.

## Slide 119: Existing Buildings Section R501.2 - Compliance
Additions, alterations, repairs or changes of occupancy to, or relocation of, existing building to comply with R502, R503, R504 or R505
If changing unconditioned space to conditioned space, comply with R502

## Slide 120: Existing Buildings Section R502 - Additions
Additions must meet the prescriptive requirements in Table R402.1.2 or R402.1.4 (R-value computation or U-factor or total UA alternatives)
N
Notes: 1. Treat the addition as a stand-alone building and ignore the common walls between the existing building and the addition.
Combine the existing building with the addition and bring the whole building to compliance. Compliance can be harder to achieve if the existing building is quite old.

## Slide 121: Existing Buildings Section R502 - Additions
Additions comply if any of the following is demonstrated
  The addition alone complies with the provisions of this code
  The existing building and addition together comply as a single building
  The existing building and addition together use no more energy than the existing building

## Slide 122: Existing Buildings Section R502 – Change in Space Conditioning
Any unconditioned or low-energy space altered to become conditioned space must fully comply with the code
Exceptions:
  If using simulated performance, annual energy cost of proposed design is allowed to be 110 percent of annual energy cost otherwise allowed by R405.2
  If Total UA of existing building AND addition AND any alterations is ≤ Total UA generated for existing building
  If complying per R405 and annual energy cost or energy use of the addition AND existing building AND any alterations is ≤ annual energy cost of the existing building
    Addition and alterations to comply with R405 in its entirety

## Slide 123: Existing Buildings Section R503 - Alterations
Code applies to any new construction
Unaltered portion(s) do not need to comply
(R503.1.1.1) Replacement fenestration that includes both glazing and sash must meet
  0.25 SHGC in Climate Zones 1-3
  0.40 SHGC in Climate Zone 4 except Marine
  U-factors in all Climate Zones 1-8
Where more than 1 replacement fenestration unit is to be installed, an area-weighted average U-factor, SHGC or both of all replacement fenestration units can be an alternative compliance approach.
Notes: The section refers to the R-value table and should also refer to the U-factor table.
When installing more than one replacement fenestration unit, an alternative is to show an area-weighted average of the U-factor, SHGC, or both

## Slide 124: Existing Buildings Section R503 - Alterations
Building Envelope
  Exceptions:
  Storm windows over existing fenestration
  Surface-applied window film installed on existing single pane
  Exposed, existing ceiling, wall or floor cavities if already filled with insulation
  Where existing roof, wall or floor cavity isn’t exposed
  Roof recover
  Roofs without cavity insulation and neither sheathing nor insulation is exposed during the reroofing
      Insulate either above or below the sheathing
    Lighting
    Exceptions:
        <10% of luminaries in a space are replaced
        Only bulbs and ballasts within existing luminaries are replaced (provided installed interior lighting power isn’t increased)
Notes: The code states that additions, alterations, renovations or repairs can’t create an unsafe or hazardous condition or overload existing building systems.
Surface applied window film installed on existing single pane fenestration assemblies to reduce solar heat gain provided the code does not require the glazing or fenestration assembly to be replaced.

## Slide 125: Existing Buildings Section R503 - Alterations
Heating and Cooling
  HVAC ducts newly installed as part of the alteration to comply with Section 403
    Exception: Where ducts from on existing HVAC system are extended to an addition
Service hot water (SHW) systems
  New SHW systems that are part of the alteration to comply with R403.5

## Slide 126: Existing Buildings Section R504 - Repairs
Work on nondamaged components necessary for the required repair or damaged components shall be considered part of the repair and are not subject to the alteration requirements
Repairs considered part of the code
  Glass-only replacements in an existing sash and frame
  Roof repairs
  Repairs where only the bulb, ballast or both within the existing luminaires in a space are replaced provided the replacement does not increase the installed interior lighting power

## Slide 127
Appendix RB – Solar-ready Provisions – Detached One- and Two-family Dwellings and Townhouses
Allows jurisdictions to adopt a model for zero energy home designation
Meant to support potential future improvements of solar electric and solar thermal systems
Applies to new construction (not additions or alterations)
Notes: Appendix RB is optional unless adopted and made mandatory by the adopting authority

## Slide 128
Appendix RC – Zero Energy Residential Building Provisions
New residential buildings
Would result in a residential building with zero net energy consumption over the course of a year
Designed to work with residential occupancies where ERI can be applied
Requires a maximum ERI first be met for building energy use only and then achieve a score of 0 when on-site power production is considered
Allows for renewable energy to be generated onsite or offsite
Notes: Appendix RC is optional unless adopted and made mandatory by the adopting authority