## Slide 1: REScheck Basics
V. Robert Salcido
Senior Engineer
2023 Department of Energy National Energy Codes Conference
Building Energy Codes Program
PNNL-SA-XXXXXX
Notes: PNNL develops and supports the CheckTools suite of software- Gate Keepers and Key Masters
Residential projects – REScheck
Commercial projects - COMcheck
Why do we do this?
Compliance: Provide technical assistance to states to implement building energy codes including increasing and verifying compliance to ensure consumer benefits (42 USC 6833), develop software to support a streamlined compliance process, provide objective information resources and technical guidance to states and localities to increase code compliance.

## Slide 2
BECP Tools used only during “Demonstrate Compliance” Stage
Demonstrate Compliance
Collect Data
Check Compliance
Plan Review
Review Software Input
Review Mandatory Requirements
Field Inspection
Verify compliance of inspection checklist items
Prepare Input
Generate Compliance Report
Check Compliance Results
Approve compliance
Builder Architect Designer
Plan Reviewer
Field Inspector
Paper/PDF
Building Energy Codes Program
REScheck Current Use Scenario
Paper/PDF
Notes: Where REScheck fits into the whole design and build process

## Slide 3
www.energycodes.gov
Notes: This is the website where you can find the REScheck software. Both web and desktop. This workshop will focus on the web as the desktop will be phased out.

## Slide 4
Building Energy Codes Program
REScheck Page
https://www.energycodes.gov/rescheck
Notes: Links directly to REScheck web and REScheck desktop

## Slide 5
Building Energy Codes Program
REScheck Currently Supported Energy Codes
Notes: Codes that REScheck supports. There are state amended codes that have been implemented that meet the DOE requirements for inclusion into REScheck.

## Slide 6
Building Energy Codes Program
Residential Energy Code Compliance
Notes: REScheck also supports a limited performance alternative: Envelope trade-offs only.

## Slide 7
Building Energy Codes Program
REScheck Supported Compliance Methods
Total UA
  Considers thermal conductance of envelope assemblies
  “Trades-off” UA from above-code assemblies to below-code assemblies
  UA = U-factor x Area for each building assembly
  Sum UA for Proposed Building compared to SUM UA for Code (Budget) Building
Performance Alternative
  Considers the whole building energy performance
  Based on simulated performance of the proposed building compared to the code standard building
  Requires additional inputs (over UA approach): building orientation, minimum of four walls having unique orientations, and a minimum of one roof and floor
  Envelope trade-off only, no mechanical equipment trade-off
Notes: Total UA – measure of the effectiveness of the thermal envelope. Considers the thermal conductance of envelope assemblies and the effect of thermal bridging.
Performance Alternative – limited in scope and only tradeoffs with envelope allowed. No tradeoffs with infiltration, mechanical, L&A or ducts can be conducted.

## Slide 8
Building Energy Codes Program
Energy Code Envelope Assembly Requirements
Notes: Energy code offers two sets of requirements. REScheck applies the U-factor set of requirements for both Total UA and Prescriptive compliance methods.

## Slide 9
Building Energy Codes Program
Walkthrough REScheck Steps
Select the appropriate energy code
Enter mechanical equipment (optional)
Review Mandatory Requirements
Reports View/print/save
Enter project information
Enter building envelope components
Register for Account Log In

## Slide 10
Building Energy Codes Program
REScheck-Web: Registration and Account Log-In
Notes: Users will be required to register from now on.
Once registration is complete, log in credentials can be saved depending on browser and company policy.

## Slide 11
Building Energy Codes Program
Home: My Projects (aka Project Dashboard)
Notes: “Home” (aka Project Dashboard) gives users advanced project management capabilities.
Standard table features exists:
Sort columns in ascending/descending order by alternately clicking on column header.
Modify projects status descriptor to identify projects that are final.
Send out sharing privileges with co-workers.
Bulk process deletion operations.
Specify “My Profile” and “My Settings” features.
Use the “Create Sample Project” button to create an example project to review and study as a tutorial aid.
Right-mouse-click on Project name to see other options specific to projects.

## Slide 12
Building Energy Codes Program
My Profile
Notes: Add co-workers to your Address Book that you wish to sharing projects with.
Your personal information will accompany share invitation emails.

## Slide 13
Building Energy Codes Program
My Settings
Notes: My Settings can be used to set default properties to invoke for each new project you create.
Toggle the default project settings on/off to temporarily disable use of defaults.

## Slide 14
Building Energy Codes Program
Project Tab: New Project
Notes: New projects will open in “edit” mode by default.
Existing (previously saved projects) will open in “read-only” mode. Click Edit to allow editing to occur.
REScheck designed flow to move from the top left to bottom right. Flow should be to move left to right and top to bottom

## Slide 15
Building Energy Codes Program
Energy Code, Location, Project Type, Compliance Method
Notes: Location of project determines climate zone.
Project type and compliance method determines what method is used for determining compliance.
2015/2018 IECC Alternation projects require prescriptive path method be used.
Trade-off compliance approach is used for New Construction and Addition.

## Slide 16
Building Energy Codes Program
Project Location Specification
Notes: Project location can be specified by typing in a zipcode, city name, county name, and/or state.
In most inputs, a drop-down list will be displayed and populated according to previously entered content while type ahead keystrokes can be matched with those inputs.

## Slide 17
Building Energy Codes Program
Project Tab: Project Type
Select New Construction, Addition or Alteration on Project screen
  Additions
  User choice:
    Addition only
    Addition plus existing home
  Alterations
    Only include those assemblies being altered
    Exemptions may apply (“Alteration Details”)

## Slide 18
Building Energy Codes Program
Building Characteristics
1- and 2-Family, Detached
Low-rise Multifamily

## Slide 19
Building Energy Codes Program
Building Characteristics: Multifamily
Multifamily if
  All multifamily buildings three stories or less in height above grade and
  Contain three or more attached dwelling units
  Examples
    Apartments
    Condominiums
    Townhouses
    Dormitories
    Rowhouses
Notes: Multifamily buildings can be considered as a whole or separate reports can be generated for each dwelling unit. If compliance is being shown for an individual unit, typically you would not include the shared components that do NOT separate conditioned space from unconditioned space. Where individual units are identical, one report may be submitted as representative of the others. Contact the authority having jurisdiction to determine which approach to take.

## Slide 20
Building Energy Codes Program
Envelope Tab

## Slide 21
Building Energy Codes Program
Envelope Helpful Hints
Don’t have to use every button
Can group “like” components
Gross area (except slab-on-grade)
  Gross wall area to include peripheral edges of floors (area of band joist and subfloor between floors)
Use “Other” assembly as needed
Notes: Use of “other” requires a U-factor of the entire assembly, not just the insulation R-value. Documentation of the calculated assembly U-factor must be provided to the local jurisdiction.

## Slide 22
Building Energy Codes Program
Color Cues
Red
Green
Notes: Colors – red usually indicates missing information, errors, or failing compliance;
Colors –green on the screen means a passing condition, in help it means a glossary term;

## Slide 23
Building Energy Codes Program
What is the Building Thermal Envelope?
Notes: Consists of ceiling, walls (above grade and below grade), fenestration, foundation

## Slide 24
Building Energy Codes Program
Entering Building Components
Enter only applicable building components

## Slide 25
Building Energy Codes Program
Envelope Tab
Notes: Multiple viewing options are available including fully collapsing (hiding) category tables, expanding them in part or in fully expanded mode.
This allows for personalizing your display to accommodate data entry and review.

## Slide 26
Building Energy Codes Program
Envelope Full View Example
Notes: Fully expanded view

## Slide 27
Building Energy Codes Program
Envelope Tab (edit mode)
Notes: Edit mode displays the time remaining before inactivity will automatically terminate a project edit session.
This is done to limit projects from being left in a locked state unintentionally.

## Slide 28
Building Energy Codes Program
Envelope Add Wall Example
Notes: This illustrates how to add an assembly. In this case an above-grade exterior wall is added by clicking the Add button in the Walls category table. The drop-down list from clicking Add will include Wall, Window, and Door. When wall is selected the screen “Add Wall Assembly” is displayed.
The type of wall assembly selected on the left hand side of the screen determine what inputs are presented on the right hand side of the screen.

## Slide 29
Building Energy Codes Program
Cavity vs. Continuous
Cavity R-value – used for insulation placed between structural members
Continuous R-value – used for insulation that is continuous across the structure (e.g., rigid insulation)

## Slide 30
Building Energy Codes Program
Envelope Glazing Requirements
Notes: Example of the Glazing Requirements screen that is displayed when clicking on the hypertext item in the background having the same name.
The requirements displayed are dependent on the energy code and location of the project as well as the set of windows/skylights that are specified.

## Slide 31
Building Energy Codes Program
Fenestration: U-Factors and SHGCs

## Slide 32
Building Energy Codes Program
Envelope Show Assembly Details
Notes: The icon at the far right of each assembly row is “Show more details” feature. It displays all data that were specified in the assembly dialog including those that may not fit well within the assembly row columns.

## Slide 33
Building Energy Codes Program
Foundations – what button to use
Basement
Basement is conditioned
Floor
Separates conditioned from ambient or unconditioned space
Crawl Wall
Crawl space is not vented to the outside and floor above is NOT insulated
Notes: Slab-on-grade is a type of floor. Slabs require input of perimeter of the slab component in linear feet. Slabs include all slab edges that are part of the building envelope and are less than 12” below grade. Edges of slab floors over 12” below grade (such as basement floors) aren’t subject to code requirements and shouldn’t be entered into the software.

## Slide 34
Building Energy Codes Program
What’s a Basement Wall?
Basement Wall – >50% below grade
Below grade
Basement wall
Exterior Wall –
<50% below grade
Below grade
Basement wall
Notes: Reminder – all foundation wall could be of same construction, walkout portion of this basement will be considered an above grade wall and subject to those requirements.

## Slide 35
Building Energy Codes Program
Basement Wall
Wall Height: If not uniform, provide an average height
Depth Below Grade: If sloped or uneven, provide an average depth below grade
Depth of Insulation
  Requirements are for full depth of basement wall (to 10 ft); REScheck allows trade offs
  If you enter insulation depth of 0, program assumes no insulation, regardless of values in the insulation fields
Continuous Insulation: Software assumes it’s exterior rigid
Cavity Insulation: Software assumes you’re furring out on the interior

## Slide 36
Building Energy Codes Program
Crawl Wall

## Slide 37
Building Energy Codes Program
Mechanical Tab – Performance Alternative Only

## Slide 38
Building Energy Codes Program
Compliance Tab
Mandatory requirements
  Air leakage
  Building mechanical systems and equipment
  Service water heating
  Duct construction, insulation, testing
For each requirement, the user
  Chooses an applicable “compliance option”
    Requirement will be met
    Exempt or Exceptions
    Requirement is Not Applicable
  Notes how compliance for applicable requirements are documented
This information is shown on the report in the “Comments/ Assumptions” column of the Inspection Checklist

## Slide 39
Building Energy Codes Program
Compliance Tab (edit mode)
Notes: Compliance tab shows the compliance results in detail and couples those with the mandatory requirements that must also be satisfied.

## Slide 40
Building Energy Codes Program
Compliance Failing – Helpful Hints
Review building plans to ensure all components are entered correctly
Confirm takeoffs (areas) are correct
Confirm insulation values
  Double check cavity vs. continuous entries
Confirm fenestration values
  Double check ratings on windows and doors (U-factor and SHGC)
Compare proposed U-factors with required U-factors
Evaluate UA data

## Slide 41
Building Energy Codes Program
Evaluate Assembly Performance
Notes: Consider the proposed and required U-factor for envelope assemblies. Note that requirement U-factor is “generalized” to covered a variety of standard construction types.

## Slide 42
Building Energy Codes Program
Reports
Choices, choose any or all
  Compliance Certificate
  Inspection Checklist
  Panel Certificate

## Slide 43
Building Energy Codes Program
Reports
Requirements
Inspection checklists set up by phase of construction
  Plan Review
  Footing/Foundation
  Rough-in
  Final

## Slide 44
Building Energy Codes Program
Reports
Notes: Reports are created by clicking on the Report button on the Compliance tab. The report consists of three sections that can be processed as necessary. Once the report process is complete, a dialog informs the user what the assigned name is and if the document is final. If is final then the REScheckWeb breadcrumb is updated to reflect that as is the Status flag for this project on the project dashboard.

## Slide 45
Building Energy Codes Program
Reports – Sample Compliance Certificate
Verify energy code, location, construction type, and conditioned floor area
Notes: Both users and code officials should do this step

## Slide 46
Building Energy Codes Program
Reports – Sample Compliance Certificate, cont

## Slide 47
Building Energy Codes Program
Reports – Sample Compliance Certificate, cont
Verify Values are Consistent with Plans
Verify Compliance Statement is Signed
Notes: For code officials

## Slide 48
Building Energy Codes Program
Envelope Sample Inspection Checklist
Notes: Foundation Inspection

## Slide 49
Building Energy Codes Program
Panel Certificate

## Slide 50
Building Energy Codes Program
REScheck-Web Project Sharing

## Slide 51
Building Energy Codes Program
Sharing Projects: Shared Project Invitation
Notes: Example of a project share email invitation.

## Slide 52
Building Energy Codes Program
Sharing Projects: Email Invitation
Shared project recipient will receive email with invitation to accept the “share”
Notes: Example of a project share email invitation.

## Slide 53
Building Energy Codes Program
Sharing Projects: Shared Projects
Notes: Example of project sharing types.

## Slide 54
Building Energy Codes Program
U.S. DOE: BECP Resources
Compliance software
Technical support
Code notes
Publications
Resource guides
Training materials www.energycodes.gov

## Slide 55
Building Energy Codes Program
THANK YOU!!!
V. Robert Salcido
victor.salcido@pnnl.gov
Building Energy Codes Program
www.energycodes.gov
BECP help desk
http://www.energycodes.gov/resource-center/help-desk
Notes: Send out note – always improving software for the future and would love your feedback on any features or operations